## Slide 1: SDN and Wireless security
Lecture 1
Intro to SDN
Saim Ghafoor

## Slide 2: Traditional networks
History
  Blackbox networking equipment
  Big name companies are managing and controlling the routing/switching devices
  Proprietary silicon chips
  Closed source operating system

## Slide 3
Technology was not designed keeping today in mind
  Massive scalability
  Multi tenant networks
  Virtualizations
  Cloud computing
  Mobility

## Slide 4: Traditional network problems
Protocols are box centric (inside router and switches)
  Difficult to configure correctly (consistency)
  Difficult to add new features (upgrades are needed)
  Difficult to debug

## Slide 5
Closed systems (vendor hardware)
  Stuck with given interfaces (CLI, SNMP etc)
  Hard to meaningful collaborate
  Vendors hesitant to open up
  No way to add new feature by yourself

## Slide 6
Design principles of Internet
  Simple
  Intelligent end-points
  Distributed control
  Results in huge complex network and hard to manage
  Billions of computers
  Tens of thousands of AS (asynchronous systems)
  Great business for selling routers

## Slide 7
Routers are complex.
Not easily extended
Topologies cannot be changed easily like load balancing cannot be applied easily.
Hardware is stable but not flexible according to the runtime requirements.
How to achieve optimal routing dynamically? Difficult with trad. Nwks.

## Slide 9: What is Network virtualization?
Representation of one or more logical topologies on the same infrastructure
Many different instantiations
  Virtual LANs (VLANs)
  Various technologies and testbeds
  Today we have VMWare, different cloud platforms

## Slide 10
Benefits of Network virtualization
  Sharing:
    multiple logical routers on a single platform
    Resource isolation in CPU, memory, bandwidth, forwarding tables etc
  Customizability
    Customizable routing and forwarding software
    General purpose CPUs for the control plane
    Network processors and FPGAs for the data plane
Example: different sites with different routers shared between multiple parties may want different connectivity and topology requirements

## Slide 11: Software defined networking
SDN is a framework to allow network administrators to automatically and dynamically manage and control a large number of network devices, services, topology, traffic paths, and packet handling (quality of services) policies using high-level languages and APIs.
Management includes provisioning, operating, monitoring, optimizing, and managing FCAPS (fault, configuration, accounting, performance, and security) in a multi-tenant environment.

## Slide 12: SDN
A network in which the control plane is physically separate from the data plane.
A single control plane controls several forwarding devices.
  Controls the network behavior from single high level control program
Deployments to solve network management problems in real networks
Two parts to the infrastructure | 
Control plane | Controllers, apps Defines the logics like how to forward the traffic
Data plane | Programmable switches Network devices that forwards the traffic

## Slide 13: Example
Router example
Basic job of the router: receiving packets, checking the routing table, forwarding the packets out.
In order to build the routing table, the router has to understand BGP, OSPF, RIP etc
What about getting the router table from somewhere else?

## Slide 14
Data centre Architecture
  Core layer
  Aggregation layer
  Access layer

## Slide 15: Where it came from
Problems in the distributed configuration
  Buggy, unpredictable
It would be easier, if any centralised controller will dictate the decisions and the forwarding behavior.

## Slide 16: Evolution
Routing architecture
4D
Open flow: In which high level controller could control the behavior of switches.

## Slide 17: Advantages
Easier to coordinate behavior among a network of devices
Load balancing, security policies
Easier to evolve – hard in conventional HW which are bundled devices
Easier to monitor from a high place – to look what is going on
Apply different CS approaches like programming, ML, mathematical models etc

## Slide 18
Virtualization
  Without worrying about where it is physically located
  How much it is
  How it is organized
Orchestration
  Should be able to control and manage thousands of devices with one command
Programmable
  Should be able to change behavior on fly
Dynamic Scaling
  Should be able to change size, quantity, capacity
Automation
  Lowers OpEx
  Reduces manual involvement
  Troubleshooting, reduce downtime, policy enforcement
  Provisioning and segmentation of resources
  Add new workloads, sites, devices, and resources
Visibility and Monitoring
Performance
  Optimise network device utilization and performance
  Traffic engineering and bandwidth management
  Capacity optimization
  Load balancing
  High utilization
Fast failure handling
Multi tenancy
  Tenancies need complete control over their addresses, topology, routing, and security
Service integration
  Load balancers
  Firewalls
  Intrusion detection Systems

## Slide 19: SDN Applications
Data Centres
Wide Area Backbone Networks
Enterprise networks
Internet exchange points
Home networks
Wireless networks
Internet of Things

## Slide 20
In Data Centres
Hyperscale operators (Google, Microsoft, Meta, Amazon): They’ve been using SDN in their private data centres for years to optimise east-west traffic, load balancing, and multi-tenant isolation. For example, Google’s B4 WAN and Microsoft’s VL2 are SDN-based fabrics.
Enterprise data centres: Many enterprises use VMware NSX, Cisco ACI, or OpenDaylight to get centralised network control, microsegmentation, and network automation.
Network slicing and security: SDN allows granular control of traffic policies, especially for microservices-based workloads.
In Cloud
Public cloud providers: AWS, Azure, and Google Cloud all use SDN under the hood to virtualise networking.
  AWS uses VPCs, security groups, and Transit Gateway implemented with SDN concepts.
  Azure’s Virtual Network (VNet) and Google Cloud’s VPC rely on SDN for programmable, multi-tenant isolation.
Multi-cloud and hybrid setups: SDN controllers (like VMware NSX-T or Open vSwitch) make it possible to stretch networks across on-prem and cloud, crucial for hybrid deployments.

## Slide 21
Customised hardware
Ethane
  Network architecture for the enterprise
  Direct enforcement of a single fine-grained network policy
  Domain controller computer flow table entries based in access control polices
  Custom switches: OpenWrt, NetFPGA, Linux
  Problem: Requires custom switches that support ethane protocol
What are we looking for?
We are looking for something that gets us the best of both worlds: that could operate on existing protocols yet wouldn’t require customising the hardware.
OpenFlow is the answer

## Slide 22: Hardware-based OpenFlow Switches
Ciena Coredirector
NEC IP8800
Juniper MX-series
HP Procurve 5400
Pronto 3240/3290
WiMax (NEC)
PC Engines
Netgear 7324

## Slide 23
Open Hardware: OpenFlow
Take the capabilities of existing hardware and open those up such that a standard control protocol could control the behavior of that hardware.
In openflow a separate controller communicate with the switches flow table to install forwarding table entries into the switch that control the forwarding behavior of the network.
Problem: to convince the vendors to open the flow table so that it can be controlled from a separate controller.

## Slide 24: OpenFlow Switches
Hardware-based OpenFlow Switches
  Commercial hardware switches with OpenFlow capability
    Network abstraction is realized by firmware upgrading
  Show high processing speed
  Have space limitation on saving the flow table entries
    Approximately store 1500 flow entries (due to expensive CAM)
  Not easy to upgrade
    Most switches only support OpenFlow up to version 1.0
Software-based OpenFlow Switches
  OpenFlow enabled software switch (runs on x86 commodity computer)
  Performance is relatively low
  Store large amount of flow entries with bound (theoretically)
  Under active development, support most recent OpenFlow spec.
Hybrid OpenFlow Switch
  A virtual switch with specialized hardware device
  Much faster than software-based switches

## Slide 25: Software-based OpenFlow Switches
OpenvSwitch (OVS)
  Overview
    A virtual switch or Virtual Ethernet Bridge (VEB)
    User-space: configuration, control
    Kernel-space: datapath (included in main Linux kernel from v3.3)
  Features
    Support OpenFlow protocol
    Support multiple tunneling protocols
      VxLAN, Ethernet over GRE, IPsec, GRE over IPsec
    Fine-grained QoS
  Main components
    ovs-vswitchd: a daemon that implements the switch
    ovsdb-server: lightweight database server that ovs-vswitch queries to
    ovs-vsctl: a utility for querying and updating the config. of ovs-vswitchd
    ovs-dpctl: a tool for configuring and monitoring the switch kernel module
    ovs-ofctl: a tool for monitoring and administering OpenFlow switches
    ovs-controller: a simple OpenFlow controller reference implementation
    openvswitch.ko: OpenvSwitch switching datapath

## Slide 26: Types of SDN
Open SDN:
  Open SDN uses open-source technologies to implement the SDN ecosystem. OpenFlow protocol is often used to control the communication between the controller and the physical and virtual devices on the data plane.
API-based SDN:
  API SDN uses application programming interfaces (APIs) to control the movement of data on the network. APIs provide the means to program the behavior of the SDN controller and network devices.
Hybrid Model:
  Hybrid Model SDN combines the elements of software-defined networking with traditional networking protocols.
Overlay SDN (hypervisor-based):
  SDN overlay refers to a networking approach that creates a virtual overlay on top of an existing physical network infrastructure.

## Slide 27
In conclusion:
  The control and data plane should be decoupled
  Using existing protocols makes deployment easier
  Open hardware allows decoupling of control
The interest in SDN has increased over the past 10 years and many ideas have evolved since its proposal in 2009.
Is OpenFLow an SDN? No, OF is just an instantiation of SDN.