## Slide 1: SDN and WN security
Week 4 Lecture 4-2
Network virtualization, Network Slicing, Data centre
Saim Ghafoor

## Slide 2: What is network virtualization?
Abstraction of the physical network
  Support for multiple logical networks running on a common shared physical substrate
  A container of network services
Aspects of the network that can be virtualized
  Nodes: virtual machines
  Links: Tunnels (ethernet GRE)
  Storage

## Slide 3: Motivation for network virtualization
One size fits all in network infrastructure
Cost
Easy management and flexibility
Rapid innovation
New forms of network control
Simplified programming and operations
SDN does not inherently abstract the details of the physical network
  SDN separates the control and data plane. NV helps SDN to achieve this.

## Slide 4: Example Virtual Network Links: EGRE
Ethernet GRE (EGRE) Tunnelling: Ethernet frames from virtual hosts are encapsulated in IP packets
  One way is to take Ethernet frames generated by applications and encapsulate them in IP packets.
  Two nodes have the appearance of being connected by a p2P ethernet link. In an actual connected multihop
Other approaches: VXLAN

## Slide 5: FlowVisor: Virtualizing Network Control
FlowVisor virtualizes network control by letting experimental traffic run in parallel on the production network with the real user and real production traffic
User (D) can let different flows be controlled by different group of researchers
Virtualization of control based on ‘flow space’(IP add, port, etc)

## Slide 6: Rapid deployment of services: Nicira Network Virtualization Platform
Deployment of new services (another application of network virtualization)
Abstraction layer between hosts and underlying network
OpenvSwitch in host hypervisors: abstraction layer
Managed by distributed controller

## Slide 7: Nicira NVP: Applications
Dynamic workload placement
  Multi-tenant data centers
  Creation of isolated virtual networks for each tenant
Dynamic security enforcement
  Central management of security policies
  Enforcement per virtual network
  Independence from VLAN limits

## Slide 8: Dynamic Scaling of Resources: Amazon VPN
Connect logically isolated VM instances to existing network
Connection to existing infrastructure via VPN
Allows customers to define their own network, address space, etc
Extend existing enterprise data center
  VPN between Amazon VPC and data center
Applications/Benefits
  Dynamic Scaling
  Disaster recovery
  Manageability

## Slide 9: Many other examples of Nw Virtualization
Wide-Area Virtual Networks
Virtual ‘Network in a Box’
  Open vSwitch, Citrix, Vyatta, OpenSolaris, Microsoft Virtual Server
Network functions virtualisation
  Unification of middlebox functions (firewalls, etc)

## Slide 10: Network slicing

## Slide 11: Network Slicing
Divides the production network into logical slices
  Each slice controls its own packet forwarding
  Users pick which slice controls their traffic
  Existing production services run in own slice
Enforce strong isolation between slices
  Actions in one slice do not affect another
Each slice can mirror a production network
  Production
  Testing
  Research

## Slide 12
Layer | Function | Visualization Idea
Infrastructure Layer | Physical network (radio, servers, routers) | A map of shared hardware nodes
Network Slice Layer | Virtualized logical slices | Colored overlays (e.g., red for eMBB, blue for URLLC)
Service Layer | Applications/services running on slices | Icons like video streaming, sensors, autonomous car

## Slide 13: Add a Slicing Layer between planes
Basic idea: Add a layer between control and data plane. So, each control slice believes that it owns the data path
The slicing layer then has the responsibility of enforcing isolation between these slices
Policies defined at the slicing layer control which slices should access or control over different parts of the data plane.

## Slide 14: Why Slice the Network?
Multiple administrative groups
  Different departments on a campus
Multiple customers
  Tenants in a shared data center
  Researchers on a shared infrastructure
Experiments vs operational network
  Support research without breaking real services
Expanding networks foot print
  Lease components in another carriers networks
Multiple services or applications in one domain

## Slide 15: Slicing: Forwarding and Policy
Data plane remains unmodified (no performance penalty)
Policy: Specifies resource limits for each slice
  Link bandwidth
  Maximum number of forwarding rules
  Topology
  Fraction of switch/router CPU

## Slide 16: Flow Space: Which packets does the slice control?
One way to slicing a control is by using a concept FlowSpace
Slices can also be defined based on group of packets who shares one or more of the fields in common.

## Slide 17: Example: FlowVisor
FlowVisor: An OpenFLow controller that acts as a transparent proxy between OpenFlow switches and multiple OpenFLow controllers.
Slices:
  any combination of switch ports (L1),
  src/dst ethernet address or type (L2),
  src/dst IP address or type (L3), and
  src/dst TCP/UDP port or ICMP code/type (L4)
Enforces isolation between each slice

## Slide 18: FlowVisor on OpenFlow
FlowVisor sits between multiple OF controllers (operating in control plane) and OF enabled switches (in dataplane)
Performs different types of policy check
  Is this rule allowed?
    If that controller is allowed to install that rule in a switch
  Who controls this packet?
    Which controller controls a particular packet?

## Slide 19
Slice | Purpose | Characteristics
eMBB | Enhanced Mobile Broadband | High throughput, video streaming
URLLC | Ultra-Reliable Low-Latency Communication | Mission-critical, low latency
mMTC | Massive Machine Type Communication | IoT devices, low power

## Slide 20: Examples: Ways to slice the network
By switch port
  Basically the same functionality as VLANs
By application (TCP port)
  Would require some more complicated access control lists
  Dynamism possible a bit more difficult without SDN
Applications:
Testing
Home networks and IoTs

## Slide 21: Multi-Tenant Data center
Single physical data center shared by many tenant users
  Customers (Amazon)
  Applications/services (Mail, Search etc)
  Developers
Challenges
  Workloads require different topologies, services
  Address space overlaps with physical network

## Slide 22: Multi-Tenant Data centre Architecture
Each host in the data center has multiple VMs
  Each host has a hypervisor with an internal switch
  Switch forwards to local VM or another hypervisor
Need: Network hypervisor to build right network abstractions for tenants
  Control Abstraction: Tenants define a set of logical network data-plane elements that they can control
  Packet abstraction: Packets sent by endpoints should see the same service as in a native network

## Slide 23: Implementing abstractions
Network hypervisor sets up tunnels between host hypervisors
  Multicast implemented as an overlay service
Physical network sees IP packets
Centralised SDN controller configures the hosts’ virtual switches
Logical Datapath implemented entirely on the sending host
Implementing Logical Datapath
Tunnels endpoints are virtual switches running on host hypervisors
  Implemented with open vSwitch
Controller cluster can
  Modify flow table entries
  Set up tunnels

## Slide 24: Controller structure
Hypervisors and physical gateways provide the controller with location and topology information
Service providers configure the controller
Forwarding state pushed to OVS via OpenFlow

## Slide 25: Challenges
Datapath design: Making software switching at end hosts fast
Scaling the computation: computing the logical datapaths and tunnels

## Slide 26: Making data path fast
Exact match flows in kernel
  User space program matches on full flow table, installs exact match in the kernel
  Future packets for the same flow are matched in kernel
Hardware offloading of encapsulated packets requires some additional tricks.

## Slide 27: Scaling controller computation
Two layer distribution controller
  Logical controllers: Compute flows and tunnels for logical datapaths
  Physical controllers: Communicate with hypervisors, gateways, and service nodes
Logical controller avoids dealing with the full mesh of tunnels

## Slide 28: What is Network Functions Virtualization?
Network functions virtualization (NFV) is the replacement of network appliance hardware with virtual machines. The virtual machines use a hypervisor to run networking software and processes such as routing and load balancing.
A new approach for deploying middlebox functions on virtual appliances in the network

## Slide 29: Why network functions virtualization?
NFV allows for the separation of communication services from dedicated hardware, such as routers and firewalls.
This separation means network operations can provide new services dynamically and without installing new hardware.
Deploying network components with network functions virtualization takes hours instead of months like with traditional networking.
The virtualized services can run on less expensive, generic servers instead of proprietary hardware

## Slide 30: How does network functions virtualization work?
Essentially, network functions virtualization replaces the functionality provided by individual hardware networking components.
This means that virtual machines run software that accomplishes the same networking functions as the traditional hardware.
Load balancing, routing and firewall security are all performed by software instead of hardware components.
A hypervisor or software-defined networking controller allows network engineers to program all of the different segments of the virtual network, and even automate the provisioning of the network.

## Slide 31
Benefits
  Reduced Capex
  Reduced time to market
  Elastic scaling
  Targeted services
  Vendor neutrality
Use cases
  Virtualized services for enterprises
  Virtual CDNs
  Virtualised mobile core networks
  Integrate production/testing

## Slide 32: Function Elements, not Middleboxes
WAN Optimizer = caching + Deduplication + compression + Encryption + Forward Error Correction + Rate Limiter
Application Firewall = IP defragmenter + Application Detection Engine + Logger + Blocker
Snort = IP Defragmenter + Pre-processing + Misuse Detection Engine + Logger