## Slide 1: SDN and Wireless Network Security
Lecture 2-1
SDN Architecture and planes
Saim Ghafoor

## Slide 2: SDN Architecture
A typical SDN architecture consists of three layers.
Application layer:
  It contains the typical network applications like intrusion detection, firewall, and load balancing
Control layer:
  It consists of the SDN controller, which acts as the brain of the network. It also allows hardware abstraction to the applications written on top of it.
Infrastructure layer:
  This consists of physical switches which form the data plane and carry out the actual movement of data packets.
The layers communicate via a set of interfaces called the northbound APIs(between application and control layer) and southbound APIs(between control and infrastructure layer).

## Slide 3: Advantages/Disadvantages of SDN
Advantages of SDN:
  Network is programmable hence can easily be modified via the controller rather than individual switches.
  Switch hardware becomes cheaper since each switch only needs a data plane.
  Hardware is abstracted, hence applications can be written on top of controller independent of switch vendor.
  Provides better security since the controller can monitor traffic and deploy security policies. For example, if the controller detects suspicious activity in network traffic, it can reroute or drop the packets.
Disadvantages of SDN: The central dependency of the network means single point of failure, i.e. if the controller gets corrupted, the entire network will be affected.

## Slide 4: Planes
In order to understand software defined networks, we need to understand the various planes involved in networking.
Data plane: All the activities involving as well as resulting from data packets sent by the end user belong to this plane. This includes:
  Forwarding of packets
  Segmentation and reassembly of data
  Replication of packets for multicasting
Control plane: All activities necessary to perform data plane activities but do not involve end user data packets belong to this plane. In other words, this is the brain of the network. The activities of the control plane include:
  Making routing tables
  Setting packet handling policies

## Slide 5
In a traditional network, each switch has its own data plane as well as control plane. The control plane of various switches exchange topology information and hence construct a forwarding table which decides where an incoming data packet has to be forwarded via the data plane.
Software defined networking (SDN) is an approach via which we take the control plane away from the switch and assign it to a centralised unit called the SDN controller. Hence, a network administrator can shape traffic via a centralised console without having to touch the individual switches.

## Slide 6: How switch decides when packet enters a switch?
The data plane still resides in the switch and when a packet enters a switch, its forwarding activity is decided based on the entries of flow tables, which are pre-assigned by the controller. A flow table consists of match fields (like input port number and packet header) and instructions. The packet is first matched against the match fields of the flow table entries.
Then the instructions of the corresponding flow entry are executed. The instructions can be
  forwarding the packet via one or multiple ports,
  dropping the packet or adding headers to the packet.
If a packet doesn’t find a corresponding match in the flow table, the switch queries the controller which sends a new flow entry to the switch. The switch forwards or drops the packet based on this flow entry.

## Slide 7: SDN Controller
In Centralized control plane system, there is a device which contains control plane of all devices. This device control the activities of data plane of all networking devices simultaneously. This device is called Controller or SDN controller.

## Slide 8
Southbound interface
  In SDN, all networking devices must be connected to controller so that it can regulate data planes of all devices. When drawing architecture of network, usually the network architect places networking devices below controller. Now according to map conventions, interface between controller and networking devices lies to south of controller. Hence, these interfaces are called Southbound Interface.
  Southbound interface is an interface between a program on controller and a program on networking device. Note that these interfaces we are discussing are software interface not physical one.

## Slide 9
Northbound Interface
  Controller need to know many information regarding network so that it can control data plane of networking devices. Provided by Network Programmer (NP).
  NP provide essential information to controller through various software or script about what functions it has to do. These softwares/scripts are placed above controller in network architecture.
  This placement of software/script makes interfaces between controller and software in north direction, according to map conventions. Hence, Interfaces between controller and softwares are called Northbound Interface. These interfaces enable programmability of network.
  All interfaces we discussed above are program based interfaces. These interfaces in a broader sense are called Application Program Interface (API).
    An API is an interface through which two program can exchange data between them.

## Slide 10: What are the control and data planes
Control plane: Logic for controlling forwarding behaviour
  Examples routing protocols, network middlebox configuration
Data plane: Forwarding traffic according to control plane logic
  Examples: IP forwarding, layer 2 switching

## Slide 11: Why separate the control and data planes?
Independent evolution and development
  The software control of the network can evolve independently of the hardware
Control from high level software program
  Control behavior using higher order programs
  Debug and check behavior more easily

## Slide 12: Opportunities: Where separation Helps
Data centers: VM migration, Layer 2 routing
Routing: More control over decision logic
Enterprise networks: Security applications
Research networks: Coexistence with production

## Slide 13
Other opportunities separating the control and data plane offers
  Dynamic access control
  Seamless mobility/migration
  Server load balancing
  Network virtualization
  Using multiple wireless access points
  Energy efficient networking
  Adaptive traffic monitoring
  Denial of service attack detection

## Slide 14: Challenges of separating Control and Data plane
Scalability: control elements responsible for many forwarding elements (often thousands +)
Reliability/Security: What happens when a controller fails or is compromised

## Slide 15: Evolution of network programming
Evolution of SDN
  RCP
  4D architecture
  OpenFlow (SDN)

## Slide 16: Routing Control Platform (RCP)
The Routing Control Platform (RCP) is a centralized forwarding solution enabling the collection of a network topology map, running an algorithm, and selecting the preferred BGP route for each router in an Autonomous System (AS).
RCP is the earliest example of control and data plane separation
Designed for ISPs to control AS and using mainly BGP
A software-based solutions that give network administrators greater control over the routing decisions within their networks.
A centralized interface for managing and distributing routing information

## Slide 17: Benefits of RCP
Enhanced Network Performance
Improved Network Resilience
Increased Security
Scalability and flexibility

## Slide 18
The RCP must have complete visibility. Otherwise, it could assign routes that create black holes, forwarding loops, or other issues preventing packets from reaching their destinations.
A potential issue with route reflection is that AS exit best path selection (hot potato routing) is performed by route reflectors from their IGP reference point, which in turn gets propagated to all RR clients scattered throughout the network. As a result, the best path selected may not be optimal for many RR clients as it depends on where the RR client is logically placed in the network.
Limited to BGP

## Slide 19
Scalability: RCP
  Problem: Must store routes and compute routing decisions for every routers
  Potentially thousands of router
Eliminate redundancy
  Store a single copy of each route
  Avoid redundant computation
Accelerate lookups
  Maintain indexes to identify affected routers
Only perform BGP routing
Reliability
Replicate RCPs
  Run multiple identical servers
Run independent replicas
  Each replica has its own feed of routes
  Each replica receives the same inputes and runs the same routing algorithm
  No need for a consistency protocol if both replicas always see the same information
Route assignment must be consistent
  Even in presence of failures and partitions
  Flooding based IGP means each replica knows which partitions it connects to

## Slide 20: 4D network architecture
The 4D Network Architecture
  Motivation
  Definitions
How 4D Terminology relates to SDN Today?

## Slide 21
Conventional IP Routers
  Management Plane
    Construct network wide view
    Configure the routers
  Control Plane
    Track topology changes
    Compute routes and install forwarding tables
  Data Plane
  Forwards, filter, buffer, mark and rate-limit Pkts
  Collect traffic statistics

## Slide 22: The 4D Planes
Decision: all management and control
  Functions that operate on view of entire network and network objectives
    Path selection and traffic engineering
    Reachability control and VPNs
Dissemination: Communication to/from routers
  Functions that support creation of network wide view
    Topology discovery
    Report measurements, status
Discovery: topology and traffic monitoring
Data: traffic handling

## Slide 23
Three Goals of 4D architecture
Network level objectives
  Configure the network, not the routers
  Minimise the maximum link utilization
  Ensuring the connectivity under all layer 2 failures
Network wide views
  Complete visibility to drive decision-making
  Traffic matrix, network topology, equipment
Direct control
  Direct, sole control over data plane configuration
  Packet forwarding, filtering, marking, buffering

## Slide 24
Goal of 4D is to remove/minimise the conventional routing plane
Faster innovation
  Remove dependence on vendors
Simpler management systems
  No need to invert control plane operations
Easier interoperability between vendors
Simpler, cheaper routers
  Little or no software on the routers
Removing the control plane from Routers
  Control software can run elsewhere
  State and computation is reasonable
  System overhead can be amortised
  Easier access to other information
  Some control can move to end hosts

## Slide 25
SDN still have a control plane, but it's not what 4D called a control plane
4D control plane is a distributed routing protocols
What we refer to as control plane todays is the Decision Plane in 4D
The dissemination plane lives on, but we call it a control channel
In RCP dissemination plane is BGP
In OpenFlow, its ‘secchan’